90-Day Appeal Period

Upon issuance of a Preliminary Flood Insurance Rate Map (FIRM) and Flood Insurance Study (FIS), there is a federally mandated 90-Day Appeal Period for public review of the data. The 90-Day Appeal Period begins on the date of the second publication of a legal notice reporting the new or revised changes in a local newspaper.  During the Appeal Period, the community or other interested parties may refute the data shown on the Preliminary FIRM or FIS report and submit a formal objection in two ways: Appeal Process and/or Comment Process.

Appeal Process

A flood study that determines BFEs along a stream involves collection of historical and physical data, follow by analyses using hydrologic methods to determine flow rates, and hydraulic modeling to determine water-surface elevations. Studies of coastal flooding involve specialized analyses of storm surge and wave effects. Depending on the specific aspect of the study that is being challenged, various types of data are required to support an appeal.

The appeal is a formal objection to new or modified BFE (or Base Flood Depths) or any change in Special Flood Hazard Area (SFHA) boundary, floodway delineation, or zone designation shown on a preliminary FIRM or in a FIS report. They can be appealed if they are shown to be scientifically or technically incorrect. The distinction between “scientifically incorrect” and “technically incorrect” is important because of the differences in the types and amounts of data needed in support of an Appeal. The basis of formal appeals is provided along with the data needed to support it in FEMA’s Criteria for Appeals of Flood Insurance Rate Maps found online at: http://www.fema.gov/media-library-data/5270aa93d5b892c8420248bc8f40a1ee/FIRM+Appeals+(EAP)+Criteria.pdf.

Comment Process

A formal objection to any new or revised information shown on a preliminary FIRM or FIS report submitted during the 90-Day Appeal Period that does not involve addition/modification of BFEs/Base Flood Depths (BFDs), or any change in SFHA boundary, floodway delineations, or flood zone designations is known as a Comment. In general, a formal Comment involves corporate limit revisions, road name errors and revisions, base map errors, and other possible omissions or potential improvements to the mapping.

Submittal of Appeal and Comment Petitions

The formal objection as either an Appeal or Comment and all supporting data shall be submitted to the Chief Executive Officer (CEO) of the community or to the local official designated by the CEO, such as the local Floodplain Administrator (FPA). It is then the community’s responsibility to forward this information to Northwest Florida Water Management (NWFWMD) for review and resolution.

The CEO or designated community official should review each formal Appeal or Comment received to first verify completeness that all supporting documentation is supplied. Then the community should prepare a statement as to whether the community supports or does not support the formal objection.  Then the community shall forward the Appeal or Comment to NWFWMD’s designee before the completion of the 90-day appeal period.

Submittal of Appeal and Comment Petitions

An Acknowledgement Letter will be sent notifying the community that an Appeal or Comment has been received by NWFWMD. The supporting data will be reviewed to determine whether it constitutes a valid Appeal or Comment and if a revision is supported. If necessary, additional supporting data may be requested during this stage. Following the review of all submitted data, an Appeal Resolution Letter will be send to the community CEO explaining the resolution of the Appeal or Comment. A revised Preliminary Transmittal Letter, disseminating a revised preliminary FIS report and/or FIRM that incorporates changes made, as a result, of the Appeal or Comment will be sent to the community, if necessary. The community has 30 days to review and comment on the resolution when necessary. At the end of the comment period and after all resolutions are completed, FEMA issues a Letter of Final Determination to the impacted community, publishes a notice about the changes in the Federal Register, and initiates the final production of the FIS report and FIRM.

All efforts will be made to incorporate revision requests into the new FIRM and FIS report. However, without receipt of the necessary data within a reasonable time frame, the revision request may require processing after the preliminary FIS report and FIRM panels become effective. A community’s effective FIRM or FIS report can be updated through the Letter of Map Revision process when all of the necessary data is submitted.

|  | APPEAL FORM | Appeal Number_____________ (For NWFWMD use only) |
| --- | --- | --- |

Scientifically Incorrect SFHAs and BFEs

| Basis of Formal Appeal | Required Data to Support Appeal | Data Certified By |
| --- | --- | --- |
| Incorrect or inappropriate methodology used in the new study | Explanation for superiority of an alternative methodology A new study using the alternative methods or assumptions that are believe to be superior to those used in the preliminary study that includes. Must submit as applicable: new hydrologic/hydraulic/coastal/floodway analyses, revised summary of discharges, flood profiles, transect data, summary of stillwater elevations table, floodway data table and revised SFHA boundaries and regulatory floodway boundaries | Certified professional engineer |
| Inappropriate or incorrect assumptions in methodology |  |  |

#### Technically Incorrect SFHAs and BFEs

| Basis of Formal Appeal | Required Data to Support Appeal | Data Certified By |
| --- | --- | --- |
| Methodology not correctly applied in the new study | Explanation for superiority of an alternative methodology A new study in which the original methodology has been applied differently. Must submit, as applicable: new hydrologic/hydraulic/coastal/floodway analyses, revised summary of discharges, flood profiles, transect data, summary of stillwater elevations table, floodway data table and revised SFHA boundaries and regulatory floodway boundaries | Certified professional engineer or Licensed land surveyor (new survey) |
| Insufficient or poor quality data in a new study | Data believed to be superior to those used in original hydrologic or hydraulic analysis; documentation for source of the new data Explanation for improvement resulting from use of new data A new study using new data: Must submit as applicable: new hydrologic and/or hydraulic analysis, flood profiles, and SFHA and regulatory floodway boundaries, using the alternative methods or data that are believed to be superior to those used in the preliminary study |  |
| Mathematical error in a new study | Information that identifies the mathematical error |  |
| Measurement error in a new study | Information that identifies the error and provides the correct measurement |  |
| Physical change in the floodplain since the new study | Information that identifies the change and sufficient topographical and/or structural data for an new hydraulic analysis Certified topographic maps or other certified ground elevation data of greater detail or more recent than those used for the preliminary SFHAs in question, preferred in Geographic Information System (GIS) format, and must adhere to FEMA’s Standards for Flood Risk Analysis and Mapping New SFHA boundaries preferred in GIS format |  |

| Name |  |
| --- | --- |
| Address |  |
| Telephone Number |  |

Please use back of page if need to submit additional panels or streams

| Panel Number | Stream Name | Basis of Formal Objection | Description of Challenged Data | Data Supporting Objection |
| --- | --- | --- | --- | --- |

The Appeal Form and all supporting documentation must be submitted to the Community Executive Officer (CEO) or to the local official designated by the CEO, such as the Floodplain Administrator, during the 90-Day Appeal Period.  It is then the community’s responsibility to forward the Appeal Petition, all supporting documentation, and the community’s statement of support or non-support for the Appeal to:
Northwest Florida Water Management District, John Crowe, 81 Water Management Drive, Havana, FL 32333, John.Crowe@nwfwater.com

| Panel Number | Stream Name | Basis of Formal Objection | Description of Challenged Data | Data Supporting Objection |
| --- | --- | --- | --- | --- |

|  | COMMENT FORM | Comment Number_____________ (For NWFWMD use only) |
| --- | --- | --- |

| Basis of Formal Comment | Required Data to Support Comment | Submitted by |
| --- | --- | --- |
| Corporate Limits, Road Names/Locations | Community maps in either digital or paper format showing the current information | Community Official, Professional Engineer, Registered Land Surveyor, or GIS Specialist |

| Name |  |
| --- | --- |
| Address |  |
| Telephone Number |  |

| Panel Number | Basis of Formal Objection | Description of Challenged Data | Data Supporting Objection |
| --- | --- | --- | --- |

The Comment Form and all supporting documentation must be submitted to the Community Executive Officer (CEO) or to the local official designated by the CEO, such as the Floodplain Administrator, during the 90-Day Appeal Period.  It is then the community’s responsibility to forward the Appeal Petition, all supporting documentation, and the community’s statement of support or non-support for the Appeal to:
Northwest Florida Water Management District, John Crowe, 81 Water Management Drive, Havana, FL 32333, John.Crowe@nwfwater.com